DEPARTMENT OF ENVIRONMENTAL qUALITY, GREAT LAKES, AND ENERGY

rEMEDIATION AND REDEVELOPMENT DIVISION

Environmental contamination response activity

Filed with the secretary of state on

These rules take effect immediately upon filing with the secretary of state unless adopted under section 33, 44, or 45a(69) of the administrative procedures act of 1969, 1969 PA 306, MCL 24.233, 24.244, or 24.245a.  Rules adopted under these sections become effective 7 days after filing with the secretary of state.

(By authority conferred on the director of the Ddepartment of Eenvironmental Quality, Great Lakes, and energy by sections 20104(1), and 20120a(18) of the natural resources and environmental protection act, 1994 PA 451, MCL 324.20104(1), and 324.20120a(18))

R 299.44 of the Michigan Administrative Code is amended, as follows:

CLEANUP CRITERIA ReQUIREMENTS for response activity

R 299.44   Generic groundwater cleanup criteria.

Rule 44. The generic groundwater cleanup criteria for all categories are shown in table 1, and table 1a.

TABLE 1.  GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Acenaphthene | 83329 | 1,300 | 3,800 | 38 | 4,200 (S) | 4,200 (S) | 4,240 | ID |
| Acenaphthylene | 208968 | 52 | 150 | ID | 3,900 (S) | 3,900 (S) | 3,930 | ID |
| Acetaldehyde (I) | 75070 | 950 | 2,700 | 130 | 1.1E+6 | 2.3E+6 | 1.00E+9 | 8.9E+6 |
| Acetate | 71501 | 4,200 | 12,000 | (G) | ID | ID | ID | ID |
| Acetic acid | 64197 | 4,200 | 12,000 | (G) | NLV | NLV | 6.00E+9 | 1.0E+9 (D) |
| Acetone (I) | 67641 | 730 | 2,100 | 1,700 | 1.0E+9 (D,S) | 1.0E+9 (D,S) | 1.00E+9 | 1.5E+7 |
| Acetonitrile | 75058 | 140 | 400 | NA | 2.4E+7 | 4.5E+7 | 2.00E+8 | 2.1E+7 |
| Acetophenone | 98862 | 1,500 | 4,400 | ID | 6.1E+6 (S) | 6.1E+6 (S) | 6.10E+6 | ID |
| Acrolein (I) | 107028 | 120 | 330 | NA | 2,100 | 4,200 | 2.10E+8 | 6.7E+6 |
| Acrylamide | 79061 | 0.5 (A) | 0.5 (A) | 10 (X) | NLV | NLV | 2.20E+9 | NA |
| Acrylic acid | 79107 | 3,900 | 11,000 | NA | 1.2E+7 | 2.8E+7 | 1.00E+9 | 1.0E+9 (D) |
| Acrylonitrile (I) | 107131 | 2.6 | 11 | 2.0 (M); 1.2 | 34,000 | 1.9E+5 | 7.50E+7 | 6.4E+6 |
| Alachlor | 15972608 | 2.0 (A) | 2.0 (A) | 11 (X) | NLV | NLV | 1.83E+5 | ID |
| Aldicarb | 116063 | 3.0 (A) | 3.0 (A) | NA | NLV | NLV | 6.00E+6 | ID |
| Aldicarb sulfone | 1646884 | 2.0 (A) | 2.0 (A) | NA | NLV | NLV | 7.80E+6 | ID |
| Aldicarb sulfoxide | 1646873 | 4.0 (A) | 4.0 (A) | NA | NLV | NLV | 2.80E+7 | ID |
| Aldrin | 309002 | 0.098 | 0.4 | 0.01 (M); 8.7E-6 | 180 (S) | 180 (S) | 180 | ID |
| Aluminum (B) | 7429905 | 50 (V) | 50 (V) | NA | NLV | NLV | NA | ID |
| Ammonia | 7664417 | 10,000 (N) | 10,000 (N) | (CC) | 3.2E+6 | 7.1E+6 | 5.30E+8 | ID |
| t-Amyl methyl ether (TAME) | 994058 | 190 (E) | 190 (E) | NA | 2.6E+5 | 5.7E+5 | 2.64E+6 | NA |
| Aniline | 62533 | 53 | 220 | 4 | NLV | NLV | 3.60E+7 | NA |
| Anthracene | 120127 | 43 (S) | 43 (S) | ID | 43 (S) | 43 (S) | 43.4 | ID |
| Antimony | 7440360 | 6.0 (A) | 6.0 (A) | 130 (X) | NLV | NLV | NA | ID |
| Arsenic | 7440382 | 10 (A) | 10 (A) | 10 | NLV | NLV | NA | ID |
| Asbestos (BB) | 1332214 | 7.0E MFL (A) | 7.0E MFL (A) | NA | NLV | NLV | NA | NA |
| Atrazine | 1912249 | 3.0 (A) | 3.0 (A) | 7.3 | NLV | NLV | 70,000 | ID |
| Azobenzene | 103333 | 23 | 94 | ID | 6,400 (S) | 6,400 (S) | 6,400 | ID |
| Barium (B) | 7440393 | 2,000 (A) | 2,000 (A) | (G) | NLV | NLV | NA | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Benzene (I) | 71432 | 5.0 (A) | 5.0 (A) | 200 (X) | 5,600 | 35,000 | 1.75E+6 | 68,000 |
| Benzidine | 92875 | 0.3 (M); 0.0037 | 0.3 (M); 0.015 | 0.3 (M); 0.073 | NLV | NLV | 5.20E+5 | ID |
| Benzo(a)anthracene (Q) | 56553 | 2.1 | 8.5 | ID | NLV | NLV | 9.4 | ID |
| Benzo(b)fluoranthene (Q) | 205992 | 1.5 (S,AA) | 1.5 (S,AA) | ID | ID | ID | 1.5 | ID |
| Benzo(k)fluoranthene (Q) | 207089 | 1.0 (M); 0.8 (S) | 1.0 (M); 0.8 (S) | NA | NLV | NLV | 0.8 | ID |
| Benzo(g,h,i)perylene | 191242 | 1.0 (M); 0.26 (S) | 1.0 (M); 0.26 (S) | ID | NLV | NLV | 0.26 | ID |
| Benzo(a)pyrene (Q) | 50328 | 5.0 (A) | 5.0 (A) | ID | NLV | NLV | 1.62 | ID |
| Benzoic acid | 65850 | 32,000 | 92,000 | NA | NLV | NLV | 3.50E+6 | ID |
| Benzyl alcohol | 100516 | 10,000 | 29,000 | NA | NLV | NLV | 4.40E+7 | ID |
| Benzyl chloride | 100447 | 7.7 | 32 | NA | 12,000 | 77,000 | 4.90E+5 | NA |
| Beryllium | 7440417 | 4.0 (A) | 4.0 (A) | (G) | NLV | NLV | NA | ID |
| bis(2-Chloroethoxy)ethane | 112265 | ID | ID | ID | NLV | NLV | 1.89E+7 | ID |
| bis(2-Chloroethyl)ether (I) | 111444 | 2 | 8.3 | 1.0 (M); 0.79 | 38,000 | 2.1E+5 | 1.72E+7 | 1.7E+7 (S) |
| bis(2-Ethylhexyl)phthalate | 117817 | 6.0 (A) | 6.0 (A) | 25 | NLV | NLV | 340 | NA |
| Boron (B) | 7440428 | 500 (F) | 500 (F) | 7,200 (X) | NLV | NLV | NA | ID |
| Bromate | 15541454 | 10 (A) | 10 (A) | 40 (X) | NLV | NLV | 38,000 | ID |
| Bromobenzene (I) | 108861 | 18 | 50 | NA | 1.8E+5 | 3.9E+5 | 4.13E+5 | ID |
| Bromodichloromethane | 75274 | 80 (A,W) | 80 (A,W) | ID | 4,800 | 37,000 | 6.74E+6 | ID |
| Bromoform | 75252 | 80 (A,W) | 80 (A,W) | ID | 4.7E+5 | 3.1E+6 (S) | 3.10E+6 | ID |
| Bromomethane | 74839 | 10 | 29 | 35 | 4,000 | 9,000 | 1.45E+7 | ID |
| n-Butanol (I) | 71363 | 950 | 2,700 | 9,800 (X) | NLV | NLV | 7.40E+7 | 4.7E+7 |
| 2-Butanone (MEK) (I) | 78933 | 13,000 | 38,000 | 2,200 | 2.4E+8 (S) | 2.4E+8 (S) | 2.40E+8 | ID |
| n-Butyl acetate | 123864 | 550 | 1,600 | NA | 6.7E+6 (S) | 6.7E+6 (S) | 6.70E+6 | 2.5E+6 |
| t-Butyl alcohol | 75650 | 3,900 | 11,000 | NA | 1.0E+9 (D,S) | 1.0E+9 (D,S) | 1.00E+9 | 6.1E+7 |
| Butyl benzyl phthalate | 85687 | 1,200 | 2,700 (S) | 67 (X) | NLV | NLV | 2,690 | ID |
| n-Butylbenzene | 104518 | 80 | 230 | ID | ID | ID | NA | ID |
| sec-Butylbenzene | 135988 | 80 | 230 | ID | ID | ID | NA | ID |
| t-Butylbenzene (I) | 98066 | 80 | 230 | ID | ID | ID | NA | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cadmium (B) | 7440439 | 5.0 (A) | 5.0 (A) | (G,X) | NLV | NLV | NA | ID |
| Camphene (I) | 79925 | ID | ID | NA | 440 | 1,000 | 33,400 | ID |
| Caprolactam | 105602 | 5,800 | 17,000 | NA | NLV | NLV | 5.25E+9 | NA |
| Carbaryl | 63252 | 700 | 2,000 | NA | ID | ID | 1.26E+5 | ID |
| Carbazole | 86748 | 85 | 350 | 10 (M); 4.0 | NLV | NLV | 7,480 | ID |
| Carbofuran | 1563662 | 40 (A) | 40 (A) | NA | NLV | NLV | 7.00E+5 | ID |
| Carbon disulfide (I,R) | 75150 | 800 | 2,300 | ID | 2.5E+5 | 5.5E+5 | 1.19E+6 | 13,000 |
| Carbon tetrachloride | 56235 | 5.0 (A) | 5.0 (A) | 45 (X) | 370 | 2,400 | 7.93E+5 | ID |
| Chlordane (J) | 57749 | 2.0 (A) | 2.0 (A) | 2.0 (M); 0.00025 | 56 (S) | 56 (S) | 56 | ID |
| Chloride | 16887006 | 2.5E+5 (E) | 2.5E+5 (E) | (FF) | NLV | NLV | NA | ID |
| Chlorobenzene (I) | 108907 | 100 (A) | 100 (A) | 25 | 2.1E+5 | 4.7E+5 (S) | 4.72E+5 | 1.6E+5 |
| p-Chlorobenzene sulfonic acid | 98668 | 7,300 | 21,000 | ID | ID | ID | NA | ID |
| 1-Chloro-1,1-difluoroethane | 75683 | 15,000 | 44,000 | NA | 3.9E+6 (S) | 3.9E+6 (S) | 3.90E+6 | NA |
| Chloroethane | 75003 | 430 | 1,700 | 1,100 (X) | 5.7E+6 (S) | 5.7E+6 (S) | 5.74E+6 | 1.1E+5 |
| 2-Chloroethyl vinyl ether | 110758 | ID | ID | NA | ID | ID | 1.50E+7 | ID |
| Chloroform | 67663 | 80 (A,W) | 80 (A,W) | 350 | 28,000 | 1.8E+5 | 7.92E+6 | ID |
| Chloromethane (I) | 74873 | 260 | 1,100 | ID | 8,600 | 45,000 | 6.34E+6 | 36,000 |
| 4-Chloro-3-methylphenol | 59507 | 150 | 420 | 7.4 | NLV | NLV | 3.90E+6 | ID |
| beta-Chloronaphthalene | 91587 | 1,800 | 5,200 | NA | ID | ID | 6,740 | ID |
| 2-Chlorophenol | 95578 | 45 | 130 | 18 | 4.9E+5 | 1.1E+6 | 2.20E+7 | ID |
| o-Chlorotoluene (I) | 95498 | 150 | 420 | ID | 2.2E+5 | 3.7E+5 (S) | 3.73E+5 | ID |
| Chlorpyrifos | 2921882 | 22 | 63 | 2.0 (M); 0.002 | 2.9 | 6.6 | 1,120 | ID |
| Chromium (III) (B,H) | 16065831 | 100 (A) | 100 (A) | (G,X) | NLV | NLV | NA | ID |
| Chromium (VI) | 18540299 | 100 (A) | 100 (A) | 11 | NLV | NLV | NA | ID |
| Chrysene (Q) | 218019 | 1.6 (S) | 1.6 (S) | ID | ID | ID | 1.6 | ID |
| Cobalt | 7440484 | 40 | 100 | 100 | NLV | NLV | NA | ID |
| Copper (B) | 7440508 | 1,000 (E) | 1,000 (E) | (G) | NLV | NLV | NA | ID |
| Cyanazine | 21725462 | 2.3 | 9.4 | 56 (X) | NLV | NLV | 1.70E+5 | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cyanide (P,R) | 57125 | 200 (A) | 200 (A) | 5.2 | NLV | NLV | NA | ID |
| Cyclohexanone | 108941 | 33,000 | 94,000 | NA | 1,500 | 3,300 | 2.30E+7 | NA |
| Dacthal | 1861321 | 73 | 210 | NA | NLV | NLV | 500 | ID |
| Dalapon | 75990 | 200 (A) | 200 (A) | NA | NLV | NLV | 5.02E+8 | ID |
| 4-4'-DDD | 72548 | 9.1 | 37 | NA | NLV | NLV | 90 | ID |
| 4-4'-DDE | 72559 | 4.3 | 15 | NA | NLV | NLV | 120 | ID |
| 4-4'-DDT | 50293 | 3.6 | 10 | 0.02 (M); 1.1E-5 | NLV | NLV | 25 | NA |
| Decabromodiphenyl ether | 1163195 | 30 (S) | 30 (S) | NA | 30 (S) | 30 (S) | 30 | ID |
| Di-n-butyl phthalate | 84742 | 880 | 2,500 | 9.7 | NLV | NLV | 11,200 | NA |
| Di(2-ethylhexyl) adipate | 103231 | 400 (A) | 400 (A) | ID | NLV | NLV | 471 | ID |
| Di-n-octyl phthalate | 117840 | 130 | 380 | ID | NLV | NLV | 3,000 | ID |
| Diacetone alcohol (I) | 123422 | ID | ID | NA | NLV | NLV | 1.00E+9 | 1.0E+9 (S) |
| Diazinon | 333415 | 1.3 | 3.8 | 1.0 (M); 0.004 | NLV | NLV | 68,800 | NA |
| Dibenzo(a,h)anthracene (Q) | 53703 | 2.0 (M); 0.21 | 2.0 (M); 0.85 | ID | NLV | NLV | 2.49 | ID |
| Dibenzofuran | 132649 | ID | ID | 4 | 10,000 (S) | 10,000 (S) | 10,000 | ID |
| Dibromochloromethane | 124481 | 80 (A,W) | 80 (A,W) | ID | 14,000 | 1.1E+5 | 2.60E+6 | ID |
| Dibromochloropropane | 96128 | 0.2 (A) | 0.2 (A) | ID | 220 | 1,200 (S) | 1,230 | NA |
| Dibromomethane | 74953 | 80 | 230 | NA | ID | ID | 1.10E+7 | ID |
| Dicamba | 1918009 | 220 | 630 | NA | NLV | NLV | 4.50E+6 | ID |
| 1,2-Dichlorobenzene | 95501 | 600 (A) | 600 (A) | 13 | 1.6E+5 (S) | 1.6E+5 (S) | 1.56E+5 | NA |
| 1,3-Dichlorobenzene | 541731 | 6.6 | 19 | 28 | 18,000 | 41,000 | 1.11E+5 | ID |
| 1,4-Dichlorobenzene | 106467 | 75 (A) | 75 (A) | 17 | 16,000 | 74,000 (S) | 73,800 | NA |
| 3,3'-Dichlorobenzidine | 91941 | 1.1 | 4.3 | 0.3 (M); 0.2 | NLV | NLV | 3,110 | ID |
| Dichlorodifluoromethane | 75718 | 1,700 | 4,800 | ID | 2.2E+5 | 3.0E+5 (S) | 3.00E+5 | ID |
| 1,1-Dichloroethane | 75343 | 880 | 2,500 | 740 | 1.0E+6 | 2.3E+6 | 5.06E+6 | 3.8E+5 |
| 1,2-Dichloroethane (I) | 107062 | 5.0 (A) | 5.0 (A) | 360 (X) | 9,600 | 59,000 | 8.52E+6 | 2.5E+6 |
| 1,1-Dichloroethylene (I) | 75354 | 7.0 (A) | 7.0 (A) | 130 | 200 | 1,300 | 2.25E+6 | 97,000 |
| cis-1,2-Dichloroethylene | 156592 | 70 (A) | 70 (A) | 620 | 93,000 | 2.1E+5 | 3.50E+6 | 5.3E+5 |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| trans-1,2-Dichloroethylene | 156605 | 100 (A) | 100 (A) | 1,500 (X) | 85,000 | 2.0E+5 | 6.30E+6 | 2.3E+5 |
| 2,6-Dichloro-4-nitroaniline | 99309 | 2,200 | 6,300 | NA | NLV | NLV | 7,000 | ID |
| 2,4-Dichlorophenol | 120832 | 73 | 210 | 11 | NLV | NLV | 4.50E+6 | ID |
| 2,4-Dichlorophenoxyacetic acid | 94757 | 70 (A) | 70 (A) | 220 | NLV | NLV | 6.80E+5 | ID |
| 1,2-Dichloropropane (I) | 78875 | 5.0 (A) | 5.0 (A) | 230 (X) | 16,000 | 36,000 | 2.80E+6 | 5.5E+5 |
| 1,3-Dichloropropene | 542756 | 8.5 | 35 | 9.0 (X) | 3,900 | 26,000 | 2.80E+6 | 1.3E+5 |
| Dichlorovos | 62737 | 1.6 | 6.7 | NA | NLV | NLV | 1.60E+7 | NA |
| Dicyclohexyl phthalate | 84617 | ID | ID | NA | ID | ID | 4,000 | ID |
| Dieldrin | 60571 | 0.11 | 0.43 | 0.02 (M); 6.5E-6 | 200 (S) | 200 (S) | 195 | ID |
| Diethyl ether | 60297 | 10 (E) | 10 (E) | ID | 6.1E+7 (S) | 6.1E+7 (S) | 6.10E+7 | 6.5E+5 |
| Diethyl phthalate | 84662 | 5,500 | 16,000 | 110 | NLV | NLV | 1.08E+6 | NA |
| Diethylene glycol monobutyl ether | 112345 | 88 | 250 | NA | NLV | NLV | 1.00E+9 | ID |
| Diisopropyl ether | 108203 | 30 | 86 | ID | 8,000 (S) | 8,000 (S) | 8,041 | 8,000 (S) |
| Diisopropylamine (I) | 108189 | 5.6 | 16 | NA | 2.1E+7 | 3.7E+7 (S) | 3.69E+7 | 4.6E+6 |
| Dimethyl phthalate | 131113 | 73,000 | 2.10E+05 | NA | NLV | NLV | 4.19E+6 | NA |
| N,N-Dimethylacetamide | 127195 | 180 | 520 | 4,100 (X) | NLV | NLV | 1.00E+9 | NA |
| N,N-Dimethylaniline | 121697 | 16 | 46 | NA | 2.4E+5 | 1.3E+6 (S) | 1.27E+6 | NA |
| Dimethylformamide (I) | 68122 | 700 | 2,000 | NA | NLV | NLV | 1.00E+9 | ID |
| 2,4-Dimethylphenol | 105679 | 370 | 1,000 | 380 | NLV | NLV | 7.87E+6 | ID |
| 2,6-Dimethylphenol | 576261 | 4.4 | 13 | NA | NLV | NLV | 6.14E+6 | ID |
| 3,4-Dimethylphenol | 95658 | 10 | 29 | 25 | NLV | NLV | 4.93E+6 | ID |
| Dimethylsulfoxide | 67685 | 2.2E+5 | 6.3E+5 | 1.9E+5 | NLV | NLV | 1.66E+8 | ID |
| 2,4-Dinitrotoluene | 121142 | 7.7 | 32 | NA | NLV | NLV | 2.70E+5 | ID |
| Dinoseb | 88857 | 7.0 (A) | 7.0 (A) | 1.0 (M); 0.48 | NLV | NLV | 52,000 | ID |
| 1,4-Dioxane (I) | 123911 | 7.2 (II) | 350 | 2,800 (X) | NLV | NLV | 9.00E+8 | 1.4E+8 |
| Diquat | 85007 | 20 (A) | 20 (A) | 20 (M); 6.0 | NLV | NLV | 7.00E+5 | ID |
| Dissolved oxygen (DO) | NA | ID | ID | (EE) | ID | ID | NA | NA |
| Diuron | 330541 | 31 | 90 | NA | NLV | NLV | 37,300 | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Endosulfan (J) | 115297 | 44 | 130 | 0.03 (M); 0.029 | ID | ID | 510 | ID |
| Endothall | 145733 | 100 (A) | 100 (A) | NA | NLV | NLV | 1.00E+8 | ID |
| Endrin | 72208 | 2.0 (A) | 2.0 (A) | ID | NLV | NLV | 250 | ID |
| Epichlorohydrin (I) | 106898 | 5.0 (M); 2.0 (A) | 5.0 (M); 2.0 (A) | NA | 3.2E+5 | 6.3E+5 | 6.60E+7 | 4.7E+7 |
| Ethanol (I) | 64175 | 1.9E+6 | 3.8E+6 | ID | NLV | NLV | 1.00E+9 | 9.7E+7 |
| Ethyl acetate (I) | 141786 | 6,600 | 19,000 | NA | 6.4E+7 (S) | 6.4E+7 (S) | 6.40E+7 | 4.2E+6 |
| Ethyl-tert-butyl ether (ETBE) | 637923 | 49 (E) | 49 (E) | ID | 2.9E+6 | 5.6E+6 (S) | 5.63E+6 | ID |
| Ethylbenzene (I) | 100414 | 74 (E) | 74 (E) | 18 | 1.1E+5 | 1.7E+5 (S) | 1.69E+5 | 43,000 |
| Ethylene dibromide | 106934 | 0.05 (A) | 0.05 (A) | 5.7 (X) | 2,400 | 15,000 | 4.20E+6 | ID |
| Ethylene glycol | 107211 | 15,000 | 42,000 | 1.9E+5 (X) | NLV | NLV | 1.00E+9 | NA |
| Ethylene glycol monobutyl ether | 111762 | 3,700 | 10,000 | NA | 2.9E+6 | 6.5E+6 | 2.24E+8 | NA |
| Fluoranthene | 206440 | 210 (S) | 210 (S) | 1.6 | 210 (S) | 210 (S) | 206 | ID |
| Fluorene | 86737 | 880 | 2,000 (S) | 12 | 2,000 (S) | 2,000 (S) | 1,980 | ID |
| Fluorine (soluble fluoride) (B) | 7782414 | 2,000 (E) | 2,000 (E) | ID | NLV | NLV | NA | ID |
| Formaldehyde | 50000 | 1,300 | 3,800 | 120 | 63,000 | 3.6E+5 | 5.50E+8 | ID |
| Formic acid (I,U) | 64186 | 10,000 | 29,000 | ID | 7.7E+6 | 1.5E+7 | 1.00E+9 | 1.0E+9 (D) |
| 1-Formylpiperidine | 2591868 | 80 | 230 | NA | ID | ID | NA | ID |
| Gentian violet | 548629 | 15 | 63 | NA | NLV | NLV | 1.00E+6 | ID |
| Glyphosate | 1071836 | 700 (A) | 700 (A) | NA | NLV | NLV | 1.16E+7 | ID |
| Heptachlor | 76448 | 0.4 (A) | 0.4 (A) | 0.01 (M); 0.0018 | 180 (S) | 180 (S) | 180 | ID |
| Heptachlor epoxide | 1024573 | 0.2 (A) | 0.2 (A) | ID | NLV | NLV | 200 | ID |
| n-Heptane | 142825 | 2,700 (S) | 2,700 (S) | NA | 2,700 (S) | 2,700 (S) | 2,690 | 200 |
| Hexabromobenzene | 87821 | 0.17 (S); 20 | 0.17 (S); 58 | ID | ID | ID | 0.17 | ID |
| Hexachlorobenzene (C-66) | 118741 | 1.0 (A) | 1.0 (A) | 0.2 (M); 0.0003 | 440 | 3,000 | 6,200 | ID |
| Hexachlorobutadiene (C-46) | 87683 | 15 | 42 | 0.053 | 1,600 | 3,200 (S) | 3,230 | ID |
| alpha-Hexachlorocyclohexane | 319846 | 0.43 | 1.7 | ID | 2,000 (S) | 2,000 (S) | 2,000 | ID |
| beta-Hexachlorocyclohexane | 319857 | 0.88 | 3.6 | ID | NLV | NLV | 240 | ID |
| Hexachlorocyclopentadiene (C-56) | 77474 | 50 (A) | 50 (A) | ID | 130 | 420 | 1,800 | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hexachloroethane | 67721 | 7.3 | 21 | 6.7 (X) | 27,000 | 50,000 (S) | 50,000 | ID |
| n-Hexane | 110543 | 3,000 | 8,600 | NA | 12,000 (S) | 12,000 (S) | 12,000 | 12,000 (S) |
| 2-Hexanone | 591786 | 1,000 | 2,900 | ID | 4.2E+6 | 8.7E+6 | 1.60E+7 | NA |
| Indeno(1,2,3-cd)pyrene (Q) | 193395 | 2.0 (M); 0.022 (S) | 2.0 (M); 0.022 (S) | ID | NLV | NLV | 0.022 | ID |
| Iron (B) | 7439896 | 300 (E) | 300 (E) | NA | NLV | NLV | NA | ID |
| Isobutyl alcohol (I) | 78831 | 2,300 | 6,700 | NA | 7.6E+7 (S) | 7.6E+7 (S) | 7.60E+7 | ID |
| Isophorone | 78591 | 770 | 3,100 | 1,300 (X) | NLV | NLV | 1.20E+7 | ID |
| Isopropyl alcohol (I) | 67630 | 470 | 1,300 | 57,000 (X) | NLV | NLV | 1.00E+9 | 6.0E+7 |
| Isopropyl benzene | 98828 | 800 | 2,300 | 28 | 56,000 (S) | 56,000 (S) | 56,000 | 29,000 |
| Lead (B) | 7439921 | 4.0 (L) | 4.0 (L) | (G,X) | NLV | NLV | NA | ID |
| Lindane | 58899 | 0.2 (A) | 0.2 (A) | 0.03 (M); 0.026 | ID | ID | 6,800 | ID |
| Lithium (B) | 7439932 | 170 | 350 | 440 | NLV | NLV | NA | ID |
| Magnesium (B) | 7439954 | 4.0E+5 | 1.1E+6 | NA | NLV | NLV | NA | ID |
| Manganese (B) | 7439965 | 50 (E) | 50 (E) | (G,X) | NLV | NLV | NA | ID |
| Mercury (Total) (B,Z) | Varies | 2.0 (A) | 2.0 (A) | 0.0013 | 56 (S) | 56 (S) | 56 | ID |
| Methane | 74828 | ID | ID | NA | (K) | (K) | NA | (AA) |
| Methanol | 67561 | 3,700 | 10,000 | 5.9E+5 (X) | 2.9E+7 (S) | 2.9E+7 (S) | 2.90E+7 | 4.5E+6 |
| Methoxychlor | 72435 | 40 (A) | 40 (A) | NA | ID | ID | 45 | ID |
| 2-Methoxyethanol (I) | 109864 | 7.3 | 21 | NA | NLV | NLV | 1.00E+9 | ID |
| 2-Methyl-4-chlorophenoxyacetic acid | 94746 | 7.3 | 21 | NA | NLV | NLV | 9.24E+5 | ID |
| 2-Methyl-4,6-dinitrophenol | 534521 | 20 (M); 2.6 | 20 (M); 7.3 | NA | NLV | NLV | 2.00E+5 | ID |
| N-Methyl-morpholine (I) | 109024 | 20 | 56 | NA | NLV | NLV | 1.00E+9 | ID |
| Methyl parathion | 298000 | 1.8 | 5.2 | NA | NLV | NLV | 50,000 | ID |
| 4-Methyl-2-pentanone (MIBK) (I) | 108101 | 1,800 | 5,200 | ID | 2.0E+7 (S) | 2.0E+7 (S) | 2.00E+7 | ID |
| Methyl-tert-butyl ether (MTBE) | 1634044 | 40 (E) | 40 (E) | 7,100 (X) | 4.7E+7 (S) | 4.7E+7 (S) | 4.68E+7 | ID |
| Methylcyclopentane (I) | 96377 | ID | ID | NA | 22,000 | 49,000 | 73,890 | ID |
| 4,4'-Methylene-bis-2- chloroaniline | 101144 | 1.1 | 4.5 | NA | NLV | NLV | 14,000 | ID |
| Methylene chloride | 75092 | 5.0 (A) | 5.0 (A) | 1,500 (X) | 2.2E+5 | 1.4E+6 | 1.70E+7 | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2-Methylnaphthalene | 91576 | 260 | 750 | 19 | 25,000 (S) | 25,000 (S) | 24,600 | ID |
| Methylphenols (J) | 1319773 | 370 | 1,000 | 30 (M); 25 | NLV | NLV | 2.80E+7 | NA |
| Metolachlor | 51218452 | 240 | 990 | 15 | NLV | NLV | 5.30E+5 | ID |
| Metribuzin | 21087649 | 180 | 520 | NA | ID | ID | 1.20E+6 | ID |
| Mirex | 2385855 | 0.02 (M); 6.8E-6 (S) | 0.02 (M); 6.8E-6 (S) | 0.02 (M); 6.8E-6 (S) | ID | ID | 6.80E-6 | NA |
| Molybdenum (B) | 7439987 | 73 | 210 | 3,200 (X) | NLV | NLV | NA | ID |
| Naphthalene | 91203 | 520 | 1,500 | 11 | 31,000 (S) | 31,000 (S) | 31,000 | NA |
| Nickel (B) | 7440020 | 100 (A) | 100 (A) | (G) | NLV | NLV | NA | ID |
| Nitrate (B,N) | 14797558 | 10,000 (A,N) | 10,000 (A,N) | ID | NLV | NLV | NA | ID |
| Nitrite (B,N) | 14797650 | 1,000 (A,N) | 1,000 (A,N) | NA | NLV | NLV | NA | ID |
| Nitrobenzene (I) | 98953 | 3.4 | 9.6 | 180 (X) | 2.8E+5 | 5.5E+5 | 2.09E+6 | NA |
| 2-Nitrophenol | 88755 | 20 | 58 | ID | NLV | NLV | 2.50E+6 | ID |
| n-Nitroso-di-n-propylamine | 621647 | 5.0 (M); 0.19 | 5.0 (M); 0.77 | NA | NLV | NLV | 9.89E+6 | ID |
| N-Nitrosodiphenylamine | 86306 | 270 | 1,100 | NA | NLV | NLV | 35,100 | ID |
| Oxamyl | 23135220 | 200 (A) | 200 (A) | NA | NLV | NLV | 2.80E+8 | ID |
| Oxo-hexyl acetate | 88230357 | 73 | 210 | NA | ID | ID | NA | ID |
| Pendimethalin | 40487421 | 280 (S) | 280 (S) | NA | NLV | NLV | 275 | ID |
| Pentachlorobenzene | 608935 | 6.1 | 17 | 5.0 (M); 0.019 | ID | ID | 650 | ID |
| Pentachloronitrobenzene | 82688 | 32 (S) | 32 (S) | NA | 32 (S) | 32 (S) | 32 | ID |
| Pentachlorophenol | 87865 | 1.0 (A) | 1.0 (A) | (G,X) | NLV | NLV | 1.85E+6 | ID |
| Pentane | 109660 | ID | ID | NA | 38,000 (S) | 38,000 (S) | 38,200 | 340 |
| 2-Pentene (I) | 109682 | ID | ID | NA | ID | ID | 2.03E+5 | ID |
| pH | NA | 6.5 to 8.5 (E) | 6.5 to 8.5 (E) | 6.5 to 9.0 | ID | ID | NA | NA |
| Phenanthrene | 85018 | 52 | 150 | 2.0 (M); 1.4 | 1,000 (S) | 1,000 (S) | 1,000 | ID |
| Phenol | 108952 | 4,400 | 13,000 | 450 | NLV | NLV | 8.28E+7 | NA |
| Phenytoin | 57410 | 17 | 68 | 89 (X) | NLV | NLV | 32,000 | ID |
| Phosphorus (Total) | 7723140 | 63,000 | 2.40E+05 | (EE) | NLV | NLV | NA | ID |
| Phthalic acid | 88993 | 14,000 | 40,000 | NA | NLV | NLV | 1.42E+7 | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Phthalic anhydride | 85449 | 15,000 | 44,000 | NA | NLV | NLV | 6.20E+6 | NA |
| Picloram | 1918021 | 500 (A) | 500 (A) | 46 | NLV | NLV | 4.30E+5 | ID |
| Piperidine | 110894 | 3.2 | 9.2 | NA | NLV | NLV | 1.00E+9 | ID |
| Polybrominated biphenyls (J) | 67774327 | 0.03 | 0.09 | ID | NLV | NLV | 1.66E+7 | ID |
| Polychlorinated biphenyls (PCBs) (J,T) | 1336363 | 0.5 (A) | 0.5 (A) | 0.2 (M); 2.6E-5 | 45 (S) | 45 (S) | 44.7 | ID |
| Prometon | 1610180 | 160 | 460 | NA | NLV | NLV | 7.50E+5 | ID |
| Propachlor | 1918167 | 95 | 270 | NA | NLV | NLV | 6.55E+5 | ID |
| Propazine | 139402 | 200 | 560 | NA | NLV | NLV | 8,600 | ID |
| Propionic acid | 79094 | 12,000 | 35,000 | ID | NLV | NLV | 1.00E+9 | 1.0E+9 (D) |
| Propyl alcohol (I) | 71238 | 1,400 | 4,000 | NA | NLV | NLV | 1.00E+9 | 7.1E+7 |
| n-Propylbenzene (I) | 103651 | 80 | 230 | ID | ID | ID | NA | ID |
| Propylene glycol | 57556 | 1.5E+5 | 4.2E+5 | 2.9E+5 | NLV | NLV | 1.00E+9 | ID |
| Pyrene | 129000 | 140 (S) | 140 (S) | ID | 140 (S) | 140 (S) | 135 | ID |
| Pyridine (I) | 110861 | 20 (M); 7.3 | 21 | NA | 5,500 | 12,000 | 3.00E+5 | 81,000 |
| Selenium (B) | 7782492 | 50 (A) | 50 (A) | 5 | NLV | NLV | NA | ID |
| Silver (B) | 7440224 | 34 | 98 | 0.2 (M); 0.06 | NLV | NLV | NA | ID |
| Silvex (2,4,5-TP) | 93721 | 50 (A) | 50 (A) | 30 | NLV | NLV | 1.40E+5 | ID |
| Simazine | 122349 | 4.0 (A) | 4.0 (A) | 17 | NLV | NLV | 4,470 | ID |
| Sodium | 17341252 | 2.3E+S(HH) | 3.5E+5 | NA | NLV | NLV | NA | ID |
| Sodium azide | 26628228 | 88 | 250 | 50 (M); 7.3 | ID | ID | NA | ID |
| Strontium (B) | 7440246 | 4,600 | 13,000 | 21,000 | NLV | NLV | NA | ID |
| Styrene | 100425 | 100 (A) | 100 (A) | 80 (X) | 1.7E+5 | 3.1E+5 (S) | 3.10E+5 | 1.4E+5 |
| Sulfate | 14808798 | 2.5E+5 (E) | 2.5E+5 (E) | NA | NLV | NLV | NA | ID |
| Tebuthiuron | 34014181 | 510 | 1,500 | NA | NLV | NLV | 2.50E+6 | ID |
| 2,3,7,8-Tetrabromodibenzo-p-dioxin (O) | 50585416 | (O) | (O) | (O) | NLV | NLV | 0.00996 | ID |
| 1,2,4,5-Tetrachlorobenzene | 95943 | 1,300 (S) | 1,300 (S) | 2.9 (X) | 1,300 (S) | 1,300 (S) | 1,300 | ID |
| 2,3,7,8-Tetrachlorodibenzo-p-dioxin (O) | 1746016 | 3.0E-5 (A) | 3.0E-5 (A) | 1.0E-5 (M); 3.1E-9 | NLV | NLV | 0.019 | ID |
| 1,1,1,2-Tetrachloroethane | 630206 | 77 | 320 | ID | 15,000 | 96,000 | 1.10E+6 | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1,1,2,2-Tetrachloroethane | 79345 | 8.5 | 35 | 78 (X) | 12,000 | 77,000 | 2.97E+6 | ID |
| Tetrachloroethylene | 127184 | 5.0 (A) | 5.0 (A) | 60 (X) | 25,000 | 1.7E+5 | 2.00E+5 | ID |
| Tetrahydrofuran | 109999 | 95 | 270 | 11,000 (X) | 6.9E+6 | 1.6E+7 | 1.00E+9 | 60,000 |
| Tetranitromethane | 509148 | ID | ID | NA | 580 | 3,200 | 85,000 | ID |
| Thallium (B) | 7440280 | 2.0 (A) | 2.0 (A) | 3.7 (X) | NLV | NLV | NA | ID |
| Toluene (I) | 108883 | 790 (E) | 790 (E) | 270 | 5.3E+5 (S) | 5.3E+5 (S) | 5.26E+5 | 61,000 |
| p-Toluidine | 106490 | 15 | 62 | NA | NLV | NLV | 7.60E+6 | NA |
| Total dissolved solids (TDS) | NA | 5.0E+5 (E) | 5.0E+5 (E) | (EE) | ID | ID | NA | NA |
| Toxaphene | 8001352 | 3.0 (A) | 3.0 (A) | 1.0 (M); 6.8E-5 | NLV | NLV | 740 | ID |
| Triallate | 2303175 | 95 | 270 | NA | ID | ID | 4,000 | ID |
| Tributylamine | 102829 | 10 | 29 | ID | 14,000 | 32,000 | 75,400 | ID |
| 1,2,4-Trichlorobenzene | 120821 | 70 (A) | 70 (A) | 99 (X) | 3.0E+5 (S) | 3.0E+5 (S) | 3.00E+5 | NA |
| 1,1,1-Trichloroethane | 71556 | 200 (A) | 200 (A) | 89 | 6.6E+5 | 1.3E+6 (S) | 1.33E+6 | ID |
| 1,1,2-Trichloroethane | 79005 | 5.0 (A) | 5.0 (A) | 330 (X) | 17,000 | 1.1E+5 | 4.42E+6 | NA |
| Trichloroethylene | 79016 | 5.0 (A) | 5.0 (A) | 200 (X) | 2,200 | 4,900 | 1.10E+6 | ID |
| Trichlorofluoromethane | 75694 | 2,600 | 7,300 | NA | 1.1E+6 (S) | 1.1E+6 (S) | 1.10E+6 | ID |
| 2,4,5-Trichlorophenol | 95954 | 730 | 2,100 | NA | NLV | NLV | 1.20E+6 | ID |
| 2,4,6-Trichlorophenol | 88062 | 120 | 470 | 5 | NLV | NLV | 8.00E+5 | ID |
| 1,2,3-Trichloropropane | 96184 | 42 | 120 | NA | 8,300 | 18,000 | 1.90E+6 | NA |
| 1,1,2-Trichloro-1,2,2-trifluoroethane | 76131 | 1.7E+5 (S) | 1.7E+5 (S) | 32 | 1.7E+5 (S) | 1.7E+5 (S) | 1.70E+5 | ID |
| Triethanolamine | 102716 | 3,700 | 10,000 | NA | NLV | NLV | 1.00E+9 | ID |
| Triethylene glycol | 112276 | 4,300 | 12,000 | NA | NLV | NLV | 1.00E+6 | ID |
| 3-Trifluoromethyl-4-nitrophenol | 88302 | 4,500 | 13,000 | NA | NLV | NLV | 5.00E+6 | ID |
| Trifluralin | 1582098 | 37 | 110 | NA | ID | ID | 8,100 | ID |
| 2,2,4-Trimethyl pentane | 540841 | ID | ID | NA | 2,300 (S) | 2,300 (S) | 2,330 | 160 |
| 2,4,4-Trimethyl-2-pentene (I) | 107404 | ID | ID | NA | ID | ID | 11,900 | ID |
| 1,2,4-Trimethylbenzene (I) | 95636 | 63 (E) | 63 (E) | 17 | 56,000 (S) | 56,000 (S) | 55,890 | 56,000 (S) |
| 1,3,5-Trimethylbenzene (I) | 108678 | 72 (E) | 72 (E) | 45 | 61,000 (S) | 61,000 (S) | 61,150 | ID |

TABLE 1. GROUNDWATER:  RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS;

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb).  One ppb is equivalent to 1 microgram per liter (ug/L).  Criteria with 6 or more digits are expressed in scientific notation.  For example, 200,000 is presented as 2.0E+5.  A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables.  When the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion (§324.20120a(10)).  In these cases, 2 numbers are present in the cell.  The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Triphenyl phosphate | 115866 | 1,200 | 1,400 (S) | NA | NLV | NLV | 1,430 | ID |
| tris(2,3-Dibromopropyl)phosphate | 126727 | 10 (M); 0.71 | 10 (M); 2.9 | ID | 4,700 (S) | 4,700 (S) | 4,700 | ID |
| Urea | 57136 | ID | ID | NA | NLV | NLV | NA | ID |
| Vanadium | 7440622 | 4.5 | 62 | 27 | NLV | NLV | NA | ID |
| Vinyl acetate (I) | 108054 | 640 | 1,800 | NA | 4.1E+6 | 8.9E+6 | 2.00E+7 | 1.8E+6 |
| Vinyl chloride | 75014 | 2.0 (A) | 2.0 (A) | 13 (X) | 1,100 | 13,000 | 2.76E+6 | 33,000 |
| White phosphorus (R) | 12185103 | 0.11 | 0.31 | NA | NLV | NLV | NA | ID |
| Xylenes (I) | 1330207 | 280 (E) | 280 (E) | 41 | 1.9E+5 (S) | 1.9E+5 (S) | 1.86E+5 | 70,000 |
| Zinc (B) | 7440666 | 2,400 | 5,000 (E) | (G) | NLV | NLV | NA | ID |

TABLE 1a. PER- AND POLYFLUOROALKYL SUBSTANCES

GROUNDWATER: RESIDENTIAL AND NONRESIDENTIAL

PART 201 GENERIC CLEANUP CRITERIA AND SCREENING LEVELS

All criteria, unless otherwise noted, are expressed in units of parts per billion (ppb). One ppb is equivalent to 1 microgram per liter (ug/L). Criteria with 6 or more digits are expressed in scientific notation. For example, 200,000 is presented as 2.0E+5. A footnote is designated by a letter in parentheses and is explained in the footnote pages that follow the criteria tables. Pursuant to section 20120a(10) of the act, MCL 324.20120a, when the risk-based criterion is less than the target detection limit (TDL), the TDL is listed as the criterion. In these cases, 2 numbers are present in the cell. The first number is the criterion (i.e., TDL), and the second number is the risk-based or solubility value, whichever is lower.

| Hazardous Substance | Chemical Abstract Service Number | Residential Drinking Water Criteria | Nonresidential Drinking Water Criteria | Groundwater Surface Water Interface Criteria | Residential Groundwater Volatilization to Indoor Air Inhalation Criteria | Nonresidential Groundwater Volatilization to Indoor Air Inhalation Criteria | Water Solubility | Flammability and Explosivity Screening Level |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Hexafluoropropylene oxide dimer acid | 13252136 | 0.37 (A) | 0.37 (A) | NA | ID | ID | NA | NA |
| Perfluorobutane sulfonic acid | 375735 | 0.42 (A) | 0.42 (A) | NA | ID | ID | NA | NA |
| Perfluorohexane sulfonic acid | 355464 | 0.051 (A) | 0.051 (A) | NA | ID | ID | NA | NA |
| Perfluorohexanoic acid | 307244 | 400 (A) | 400 (A) | NA | ID | ID | NA | NA |
| Perfluorononanoic acid | 375951 | 0.006 (A) | 0.006 (A) | NA | ID | ID | NA | NA |
| Perfluorooctanoic acid (DD) | 335671 | 0.008 (A) | 0.008 (A) | 12 (X) | ID | ID | 9.50E+06 | NA |
| Perfluorooctane sulfonic acid (DD) | 1763231 | 0.016 (A) | 0.016 (A) | 0.012 (X) | NLV | NLV | 3.1 | NA |