## Slide 1: Proposed PFAS Maximum Contaminant Levels (MCLs) and Rules
Eric Oswald
Drinking Water and Environmental Health
Steve Sliver
MPART Executive Director
Aaron Keatley
Chief Deputy
Director

## Slide 2: Background
Michigan PFAS Action Response Team
  Unique, multi-agency approach
  Data-driven and science-based
  Identify and reduce exposures
PFAS emerge in public water supplies
Executive Directive to develop rules

## Slide 3: Timeline - PFAS MCL Process
March 26, 2019: Governor Whitmer Directive
April – June 2019: MPART Science Advisory Workgroup Develops Health Based Values
July 2019: Stakeholder Listening Sessions
August 2019: EGLE Drafts Rule
September 2019: Stakeholder Meetings
September 2019: EGLE Revises Rule
October 2019: Final Draft Rule
November 2019: ERRC
December 6, 2019 – January 31, 2020: Public Comment Period
January 2020: Public Hearings
February 27, 2020: ERRC Final Vote

## Slide 4: Stakeholders Involved
Industrial Group
  Michigan Chamber of Commerce
  Michigan Chemistry Council
  Michigan Groundwater Association
  Michigan Manufactured Housing Association
  Michigan Manufacturers Association
  Michigan Waste and Recycle Association
Health Group
  District Health Departments 2 and 4
  Ionia County Health Department
  Kent County Health Department
  Michigan Association for Local Public Health
  Michigan Association of Local Environmental Health Administrators
  MDHHS

## Slide 5: Stakeholders Involved (cont.)
Environmental Group
  Clean Water Action
  Environment Michigan
  Great Lakes Environmental Law Center
  Huron River Watershed Council
  League of Conservation Voters
  Michigan Environmental Council
  National Resources Defense Council
  The Nature Conservancy
  Sierra Club

## Slide 6: Stakeholders Involved (cont.)
Municipalities Group
  AWWA
  Consultant – Prein and Newhoff
  Contractor Operations/Consultant - Fleis & VandenBrink Engineering, Inc.
  Michigan Chapter of American of Public Works Administration
  Michigan Environmental Laboratory Association
  Michigan Municipal League
  Michigan Rural Water Association
  Michigan Townships Association
  Michigan Water Environment Association
  Safe Water Engineering
  SEMCOG
  Water Utility – City of Ann Arbor
  Water Utility – Plainfield Township

## Slide 7: Stakeholders Involved (cont.)
Citizens Group
  Held 2 Webinars with Citizens in Affected Communities
  Utilized MPART Citizens Advisory Council List
  One Listening Session
  One Session to Present Draft Rules and Get Input

## Slide 8: Environmental Rules Review Committee
Janet Barlow (I), Clio Representing a statewide organization that represents small businesses Term expires 10/4/2020 | Rob Nederhood (I), Grosse Pointe Park Representing the general public Term expires 10/4/2022
Charles Lippstreu (D), Grand Rapids Representing a statewide agriculture organization Term expires 10/4/2021 | Eric Pessell, (I), Delton Representing public health professionals Term expires 10/4/2020
Dr. Melissa Stults (D), Ann Arbor Representing local governments Term expires 10/4/2021 | Daniel Frakes (I), St. Clair Shores Representing a statewide manufacturing organization Term expires 10/4/2020
David Maness (R), Midland Representing the oil and gas industry Term expires 10/4/2022 | Helen Taylor (I), Okemos Representing a statewide land conservancy organization Term expires 10/4/2022
Fadi Mourad (I), Farmington Hills Representing public utilities that engage in the generation, transmission, or distribution of electricity Term expires 10/4/2022 | Grant Trigger (I), West Bloomfield Representing the general public Term expires 10/4/2021
Shayna Schupan Barry (I), Portage Representing the solid waste management industry Term expires 10/4/2021 | Jeremy Orr (D), Detroit Representing a statewide environmental organization Term expires 10/4/2021

## Slide 9: Proposed MCLs
Contaminant | MCL (ng/L) | Effective Date | Chemical Abstract Services Registry Number (CASRN)
PERFLUORONONANOIC ACID (PFNA) | 6 | Immediate | 375-95-1
PERFLUOROOCTANOIC ACID (PFOA) | 8 | Immediate | 335-67-1
PERFLUOROOCTANE SULFONIC ACID (PFOS) | 16 | Immediate | 1763-23-1
PERFLUOROHEXANE SULFONIC ACID (PFHxS) | 51 | Immediate | 355-46-4
HEXAFLUOROPROPYLENE OXIDE DIMER ACID (HFPO-DA) (a GenX compound) | 370 | Immediate | 13252-13-6
PERFLUOROBUTANE SULFONIC ACID (PFBS) | 420 | Immediate | 375-73-5
PERFLUOROHEXANOIC ACID (PFHxA) | 400,000 | Immediate | 307-24-4

## Slide 10: How Does the Rule Work?
Applicability
Sampling Requirements
Reporting
Proposed MCLs
Compliance Calculation
Public Notification
Treatment Technologies
Laboratory Certification

## Slide 11: Who Must Follow the New Rule
Community Water Supplies
  1,400 Supplies
Non-transient Noncommunity Water Supplies
  1,300 Supplies
EGLE can require sampling of other regulated supplies

## Slide 12: Sampling Requirements
General Requirements:
  Sample where treated water enters the distribution system
  EGLE may require confirmation sampling
  EGLE may require more frequent sampling (variations in system)

## Slide 13: Sampling Requirements (cont.)
Initial Sampling:
  Modeled to ensure those with least amount of data sample first
  Must sample immediately
  Systems with data sample within 6 months
Ongoing Sampling:
  Quarterly: Supplies with detections
  Annually: Supplies with no detections or consistently below proposed MCLs

## Slide 14: When are Results Reported to EGLE?
In accordance with existing requirements:
  Within first 10 days of the month following the month in when results are received, or,
  Within 10 days of the end of the monitoring period
  ***Whichever is sooner

## Slide 15: Compliance Calculation
Compliance based on annual average at each sampling point
One point can cause the supply to be out of compliance
Positive detections result in quarterly sampling
One sample can cause the supply to exceed MCL immediately
If confirmation sampling is required, the confirmation result(s) will normally be averaged with the first result
EGLE may exclude results of obvious sampling errors

## Slide 16: Public Notification
Required if a supply is in noncompliance and to be conducted consistent with existing public notification requirements for similar contaminants.
  If a water supply is out of compliance with an MCL, a 30-day public notification is required
  Notice requires mandatory language about the source of each contaminant in drinking water and mandatory health effects language
  For community water supplies, violations must also be referenced in annual water quality reports (consumer confidence reports)

## Slide 17: Treatment Technology
Best Available: Granular Activated Carbon
  Cost used for Regulatory Impact Statement
  Capable of treating to MCLs
  Waste Stream/Regeneration
Filtration
  Produces Concentrated Waste Stream to?
Ion Exchange

## Slide 18: Laboratory Certification
Requires an EPA Certified Method
Minimum Detection Capability Required
Third Party Proficiency Testing

## Slide 19: Regulatory Impact Statement
Cost for Sampling and Analysis: $6.4M
Treatment Installation: $11M
Treatment O&M: $326K annually
Benefits addressed qualitatively
Notes: Cost are conservative, worst case

## Slide 20
Michigan Department of
Environment, Great Lakes, and Energy
www.Michigan.gov/EGLE
Sign up for email updates
Subscribe to our YouTube Channel
Follow us on Twitter @MichiganEGLE