DEPARTMENT OF ENVIRONMENT, GREAT LAKES AND ENERGYENVIRONMENTAL QUALITY

AIR QUALITY DIVISION

AIR POLLUTION CONTROL

Filed with the secretary of state on

These rules become effective immediately after filing with the secretary of state unless adopted under section 33, 44, or 45a(9) of the administrative procedures act of 1969, 1969 PA 306, MCL 24.233, 24.244, or 24.245a. Rules adopted under these sections become effective 7 days after filing with the secretary of state.

(By authority conferred on the director of the department of environment, Great Lakes, and energy environmental quality by sections 5503 and 5512 of the natural resources and environmental protection act, 1994 PA 451, MCL 324.5503 and 324.5512, and Executive Reorganization Order Nos. 1995-168, 2009-31, 2011-1, and 2019-1, MCL 324.99903, 324.99919, 324.99921, and 324.99923)

R 336.1703, R 336.1704, R 336.1705, and R 336.1706 of the Michigan Administrative Code are rescinded, as follows:

PART 7. EMISSION LIMITATIONS AND PROHIBITIONS--

NEW SOURCES OF VOLATILE ORGANIC COMPOUND EMISSIONS

R 336.1703  Loading  gasoline  into  new  stationary  vessels  of  more  than 2,000-gallon capacity at dispensing facilities.Rescinded.

Rule 703.  (1)  It is unlawful for a person to load or allow the loading  of gasoline from a delivery vessel into any new stationary vessel of  more  than 2,000-gallon capacity located at any  gasoline  dispensing  facility,  unless such stationary vessel is equipped with a permanent submerged fill pipe.

(2)  It is unlawful for a person to load or allow the  loading  of  gasoline from  a  delivery  vessel  into  any  new  stationary  vessel  of  more  than 2,000-gallon capacity located at a new gasoline  dispensing  facility  or  an existing gasoline dispensing facility subject to R 336.1606(3) and (4) in any area listed in table 61, unless the stationary  vessel  is  controlled  by  a vapor balance  system  or  an  equivalent  control  system  approved  by  the department.  The vapor balance system shall capture displaced gasoline  vapor and air via a vaportight collection line and shall be designed to return  not less than 90% by weight of the displaced gasoline vapor from the  sta-tionary vessel to the delivery vessel.

(3)  Any stationary vessel subject to subrule (2)  of  this  rule  shall  be equipped, maintained, or controlled with both of the following:

(a)  An interlocking system or  procedure  to  ensure  that  the  vaportight collection line is connected before any gasoline can be loaded.

(b)  A device to ensure that the vaportight collection line shall close upon disconnection so as to prevent release of gasoline vapor.

(4)  Any delivery vessel subject to  subrule  (2)  of  this  rule  shall  be vaportight and shall be filled only at a loading facility  that  is  equipped with a system as required in R 336.1606(3) and (4), R 336.1609(2) and (3),  R 336.1705(2) and (3), or R 336.1706(2) and (3).

(5)  A new stationary vessel at a gasoline dispensing facility that  is  not subject to the provisions of subrules (2) and  (3)  of  this  rule  shall  be constructed in a  manner  that  will  allow  the  vessel  to  be  retrofitted according to subrules (2) and (3) of this rule.

R 336.1704  Loading  gasoline  into  new  stationary  vessels  of  more  than 2,000-gallon capacity at loading facilities.Rescinded.

Rule 704.  (1)  It is unlawful for a person to load or allow the loading  of gasoline from a delivery vessel into any new stationary vessel of  more  than 2,000-gallon capacity located at any gasoline loading  facility,  unless  the stationary vessel is equipped with a permanent submerged fill pipe.

(2)  It is unlawful for a person to load or allow the  loading  of  gasoline from  a  delivery  vessel  into  any  new  stationary  vessel  of  more  than 2,000-gallon capacity located at any of  the  following  loading  facilities, unless the stationary vessel is controlled by a vapor balance  system  or  an equiva-lent control system approved by the department:

(a)  A new loading facility located in any area listed in table 61.

(b) A new loading facility located in any area not listed in table  61  that delivers  gasoline  to  a  gasoline-dispensing  facility   subject   to   the provi-sions of R 336.1606(3) and (4) or R 336.1703(2) and (3).

(c)  An existing loading facility subject to the provisions of R 336.1607(3) and (4).The vapor balance system shall capture displaced gasoline vapor and air  via a vaportight collection line and shall be designed to return  not  less  than 90% by weight of the displaced gasoline vapor from the stationary  vessel  to the delivery vessel.

(3)  Any stationary vessel subject to subrule (2)  of  this  rule  shall  be equipped, maintained, or controlled with all of the following:

(a)  An interlocking system or  procedure  to  ensure  that  the  vaportight collection line is connected before any gasoline can be loaded.

(b)  A device to ensure that the vaportight collection line shall close upon disconnection so as to prevent release of gasoline vapor.

(c)  Pressure-vacuum relief valves on aboveground  stationary  vessels  that have a minimum pressure valve setting of 8 ounces, if such setting  does  not exceed the container's maximum pressure rating.

(4)  Any delivery vessel subject to  subrule  (2)  of  this  rule  shall  be vaportight.

(5)  A person responsible for the operation of all control measures required by this rule shall develop  written  procedures  for  the  operation  of  all control measures specified in subrule (3) of this rule,  and  the  procedures shall be posted in an accessible, conspicuous location  near  the  stationary vessel.

(6)  A new stationary vessel at a gasoline  loading  facility  that  is  not subject to the provisions of subrules (2) and  (3)  of  this  rule  shall  be constructed in a manner that allows the vessel to be retrofitted according to subrules (2) and (3) of this rule.

R 336.1705  Loading gasoline into delivery vessels at new loading  facilities handling less than 5,000,000 gallons per year.Rescinded.

Rule 705.  (1)  It is unlawful for a person to load, or  allow  the  loading of, gasoline from a stationary vessel into  any  delivery  vessel  at  a  new loading facility that has a throughput of less  than  5,000,000  gallons  per year, unless the delivery vessel is filled by a submerged fill pipe.

(2)  It is unlawful for a person to load, or allow the loading of, gasoline from a stationary vessel into any delivery vessel located at  either  of  the following loading facilities that has a throughput  of  less  than  5,000,000 gallons per year, unless the delivery vessel is controlled by a vapor balance system or an equivalent control system approved by the department:

(a)  A new loading facility located in any area listed in table 61.

(b) A new loading facility located in any area which is not listed in  table 61 that delivers gasoline to a  gasoline-dispensing  facility  subject  to  R 336.1606 (3) and (4) or R 336.1703(2) and (3).The vapor balance system shall capture displaced gasoline vapor  and  air  by means of a vaportight collection line and shall be  designed  to  return  not less than 90%, by weight, of the displaced gasoline vapor from  the  delivery vessel to the stationary vessel.

(3)  Any delivery vessel that is loaded at a facility subject to subrule (2) of this rule shall be equipped, maintained, or controlled  with  all  of  the following:

(a)  An interlocking system or  procedure  to  ensure  that  the  vaportight collection line is connected before any gasoline can be loaded.

(b)  A device to ensure that the vaportight collection line shall close upon disconnection so as to prevent the release of gasoline vapor.

(c)  A device or  procedure  to  accomplish  complete  drainage  before  the loading device is disconnected, or a device or procedure  to  prevent  liquid drainage from the loading device when not in use.

(d)  Pressure-vacuum relief valves that are vaportight and  set  to  prevent the emission of displaced gasoline vapor during the loading of  the  delivery vessel, except under emergency conditions.

(e)  Hatch openings that are kept closed and vaportight during  the  loading of the delivery vessel.

(4)  Any stationary vessel at a facility subject to subrule (2) of this rule shall be vaportight.

(5)  A person who is responsible for the operation of all  control  measures required by this rule shall develop written procedures for the  operation  of all the control measures.  The procedures shall be posted in an  accessi-ble, conspicuous location near the loading device.

R 336.1706  Loading delivery vessels with organic compounds having a truevapor pressure of more than 1.5 psia at new loading facilities handling5,000,000 or more gallons of such compounds per year.Rescinded.

Rule 706.  (1)  It is unlawful for a person to load, or allow  the  loading of, any organic compound that has a true vapor pressure of more than 1.5 psia at actual conditions from any stationary  vessel  into  any  delivery  vessel located at a new loading facility that has a throughput of 5,000,000 or  more gallons of such compounds per year, unless such delivery vessel is filled  by a submerged fill pipe.

(2)  It is unlawful for a person to load, or  allow  the  loading  of,  any organic compound that has a true vapor pressure of  more  than  1.5  psia  at actual conditions from any stationary vessel into any delivery vessel located at a new loading facility that has a throughput of 5,000,000 or more  gallons of such compounds per year, unless such delivery vessel is  controlled  by  a vapor recovery system that captures all displaced organic vapor  and  air  by means of a vapor-tight collection line and recovers the  organic  vapor  such that emissions to the atmosphere do not exceed 0.7 pounds  of  organic  vapor per 1,000 gallons of organic compounds loaded.

(3)  Any delivery vessel at a facility that is subject to the provisions of subrule (2) of this rule shall be equipped, maintained,  or  controlled  with all of the following:

(a)  An interlocking system or procedure to  ensure  that  the  vapor-tight collection line is connected before any organic compound can be loaded.

(b)  A device to ensure that the vapor-tight collection  line  shall  close upon disconnection so as to prevent release of organic vapor.

(c)  A device to accomplish complete drainage before the loading device  is disconnected, or a device to prevent liquid drainage from the loading  device when not in use.

(d)  Pressure-vacuum relief valves that are vapor-tight and set to  prevent the emission of displaced organic vapor during the loading  of  the  delivery vessel, except under emergency conditions.

(e)  Hatch openings that are kept closed and vapor-tight during the loading of the delivery vessel.

(4)  A person who is responsible for the operation of all control  measures required by this rule shall develop written procedures for the  operation  of all such control measures.  Such procedures shall be posted in an accessible, conspicuous location near the loading device.

(5)  The provisions of this rule shall not apply to the  loading  of  crude oil or condensate into delivery vessels at  production  facilities,  if  such loading is accomplished with a submerged fill pipe.